## Slide 1
SEMINAR AUTONOMOUS SYSTEMS
Interfacing a Five-Finger Dexterous
Hand with a UR5e Arm
Use cases and interfacing — a design and evaluation-plan study
Siddharth Patni
Ostfalia University of Applied Sciences · Wolfenbüttel
Prof. Dr.-Ing. Sebastian Ohl
Design-stage study — hardware ordered, evaluation pending
Notes: Good morning. This seminar presents the design for attaching an Inspire five-finger dexterous hand to our lab's UR5e collaborative arm. I'll be clear up front: the hardware is on order but not yet integrated, so this is a design and evaluation-plan study — there are no experimental results yet, and I've been careful to separate verified specifications from engineering reasoning and from planned work.

## Slide 2
PART I
Introduction
Why this project, and what it sets out to answer
I
Notes: Part one: the motivation, the gap in existing work, the objectives, and — importantly — the honest scope of what this paper claims.

## Slide 3
BACKGROUND & MOTIVATION
Grippers are simple; hands are capable
Most collaborative arms carry a two-finger gripper: robust and easy to control, but able to oppose along only one axis, and unable to re-orient what it holds. Human manipulation — using tools, opening containers, handing objects over — relies on a far richer set of grasps and on the sense of touch.
Two-finger parallel gripper
One actuated DOF, one fixed opposition axis
Objects must present two parallel faces
No in-hand re-orientation
No tripod grasp, gesture, or trigger actuation
Contact sensing only if bolted on externally
Five-finger dexterous hand
Six actuators, twelve joints — thumb vs. four fingers
Wrap, pinch, tripod, and lateral grasps
Hold an object and actuate a control
Communicative gestures as posture vectors
Eight tactile sensors on the same bus
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
3
Notes: The contrast is the motivation. A parallel gripper is fine when a task reduces to one squeeze axis, but it fails the moment you need a third contact, differentiated finger roles, or contact feedback. The dexterous hand covers those cases — and crucially it has tactile sensing built into the same communication bus, which we'll use later for force-controlled grasping.

## Slide 4
OBJECTIVES
Two research questions
Q1
Q2
How is the hand interfaced?
Mechanically, electrically, and in software — so that arm and hand are driven from one coherent control stack.
What does it make possible?
Which application classes become feasible that a parallel gripper cannot deliver, within the scope of a student project.
The paper answers both at the design level and contributes:
1
Characterisation
of both platforms from vendor documentation
2
Integration design
mechanics, power, comms, software
3
Use-case mapping
five families onto verified capability
4
Evaluation plan
a pre-registered three-stage protocol
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
4
Notes: Two questions drive the work: an interfacing question and a use-case question. From them come four contributions — a specification-level characterisation, the integration design itself, a mapping of use cases onto what the hardware can actually do, and a concrete evaluation plan.

## Slide 5
SCOPE
What this study is — and is not
IT IS
A verified integration design
grounded entirely in vendor specifications
An engineering analysis of the constraints
— the power budget, the interface, the mounting
A pre-registered evaluation plan
with measurable metrics for each stage
IT IS NOT
An experimental paper
the hardware is ordered, not yet integrated
A source of measured results
no current, latency, or success rates are reported
A new algorithm or controller
the contribution is the integration, not new theory
Verified specifications, engineering reasoning, and planned work are kept explicitly distinct throughout the paper.
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
5
Notes: This slide is deliberate. Being explicit about scope is what keeps the work honest and defensible: it is a design, an analysis of constraints, and a validation plan. It is not an experimental paper, it reports no measured numbers, and it does not claim a new algorithm. Reviewers respond well to this clarity.

## Slide 6
PART II
Approach & System Design
From two datasheets to an integration design
II
Notes: Part two walks through the approach: the two platforms, why one specific hand variant is required, the central electrical finding, the two power options, and the software architecture.

## Slide 7
THE HARDWARE
Two vendor-specified platforms
Inspire RH56F1-E2R-T1
Right hand · tactile · RS-485
6 / 12
actuators / joints
630 g
mass
5 A
peak current (24 V)
≥15 N
thumb fingertip force
8
tactile sensors
RS-485
control interface
Universal Robots UR5e
Collaborative six-axis arm
5 kg
payload
850 mm
reach
±0.03 mm
repeatability
1.5 A
tool I/O supply
M8 8-pin
tool connector
RS-485
via Tool Comm. Interface
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
7
Notes: The hand: six actuators driving twelve joints, 630 grams, a 5-amp peak draw, at least 15 newtons at the thumb, eight tactile sensors, and — key for us — an RS-485 interface. The arm: 5-kilo payload, sub-tenth-millimetre repeatability, and a tool connector that supplies up to 1.5 amps and carries an RS-485 bus. Note the two RS-485 lines at the bottom of each card — that's the match we build on. And note the 5 A against the 1.5 A — that's the tension.

## Slide 8
DESIGN DECISION
Why the E2R-T1 build is uniquely determined
The series ships in four builds. The target arm — not the application — fixes the choice.
1
Interface must be RS-485
The UR5e flange carries RS-485, not CAN FD
Rules out the E4 (CAN FD) builds
→
2
Force control needs touch
Fragile-object grasping needs tactile feedback
Requires the “-T1” tactile build
→
3
Right hand ordered
Handedness set by procurement
Selects the “R” models
Result: RH56F1-E2R-T1 — the only build that satisfies all three constraints.
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
8
Notes: A small but real design finding: the variant isn't a free choice. Three constraints — RS-485 because that's what the flange carries, tactile because our fragile-grasping use case needs it, and right-handed because that's what was ordered — narrow the four builds down to exactly one. The general lesson: the arm's tool interface, not the application, usually decides the end-effector variant.

## Slide 9
THE CENTRAL FINDING
The binding constraint is electrical
120 W
Hand peak demand
24 V × 5 A
36 W
Tool connector limit
24 V × 1.5 A
≈ 30%
of peak power available
at the flange
120 W
36 W
The flange alone cannot drive high-force actuation of all fingers at once. This single mismatch shapes the whole power design.
Notes: This is the heart of the paper. The tool connector can deliver 36 watts; the hand's peak demand is 120. So the flange supplies only about thirty percent of the hand's peak power. That means you cannot power a full-force grasp of all fingers straight from the tool connector. Everything in the power design follows from this one number — and it generalises to any hungry end-effector on an e-Series arm.

## Slide 10
POWER DESIGN
Two ways to resolve the mismatch
Concept A
Flange-integrated
Powered from the 24 V tool supply over the TCI
No external cable — mechanically simplest
Current capped by the hand's registers
Reduced grip force and slower closing
Viable for light grasping only
DEFAULT
Concept B
External supply, flange comms
Dedicated 24 V supply rated ≥ 5 A along the arm
Full force and speed envelope preserved
RS-485 still via the TCI (USB fallback)
One extra cable + shared-ground bonding
Chosen: grasp-force experiments are planned
Concept A stays as a demonstrator of the simplest integration — attempted once the true current profile is measured in Stage 1.
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
10
Notes: Two clean resolutions. Concept A keeps everything on the tool connector and simply limits the current in firmware — elegant, but it derates the hand to light grasping. Concept B adds a dedicated power supply along the arm and keeps only the data on the flange — one extra cable, full force. Since we plan grasp-force experiments, deliberately weakening the hand would confound them, so Concept B is our default. Concept A stays as a clean-integration demo once we've measured the real current.

## Slide 11
SOFTWARE & COMMUNICATION
One control PC, two channels
Control PC
ROS 2 driver + hand node
MoveIt 2 · register I/O
→
TCP :54321
UR controller
ToolComm URCap + socat
relay on port 54321
→
RS-485
RH56F1-E2R-T1
register-based hand
over RS-485
UR5e arm — commanded on the driver's own Ethernet channel, separate from the hand
Reuse
the robot's own serial channel — no added fieldbus
Thin driver
effort is a small register wrapper, not transport plumbing
Latency
register round-trips over the relay are measured in Stage 1
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
11
Notes: The software runs on one Linux PC. The arm goes over Ethernet through the UR ROS 2 driver with MoveIt. The hand goes over RS-485: the vendor URCap relays the tool serial port to TCP port 54321, and socat turns that back into a local serial device the hand driver opens normally. Two takeaways — we reuse the robot's own channel instead of adding hardware, and the coding effort collapses to a thin register wrapper. The one thing we don't yet know is the relay latency; that's measured in Stage 1.

## Slide 12
USE CASES
Five capabilities beyond a gripper
1
Grasp benchmark
Reproduce taxonomy grasp types; measure success and tolerance
2
Fragile grasping
Force-thresholded closing on cups, fruit, thin-walled items
3
Teleoperation
Retarget human hand pose; collect demonstration data
4
Handover & gesture
Tactile release on tug; pointing and thumbs-up as postures
5
Lab handling
Wrap grasps, tools, and trigger-operated devices
The distinguishing axis
Integrated contact sensing in the loop — and every case is grounded in specs, none performed yet.
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
12
Notes: Five application families the combined system enables: a grasp benchmark, force-controlled fragile grasping, teleoperation for data collection, tactile handover and gesture, and general lab handling. What ties them together — and what a parallel gripper lacks — is distributed touch inside the control loop. I want to be clear: these are enabled by the specifications; none has been demonstrated yet.

## Slide 13
PART III
Findings & Evaluation
What the design shows, and how it will be tested
III
Notes: Part three: the concrete findings, the plan to validate them, the risks and limitations, and the conclusion.

## Slide 14
FINDINGS
What the design analysis establishes
1
Compatible at the flange
The hand's RS-485 meets the UR5e Tool Communication Interface — no extra fieldbus
2
Electrical is the one hard limit
5 A peak vs 1.5 A supply: only ~30% of peak power at the flange
3
Two clean power resolutions
External supply (default) or register current limiting
4
Variant uniquely determined
RS-485 + tactile + right hand → the E2R-T1 build
5
Software is a thin driver
Register access over the vendor relay; bandwidth is not the bottleneck
6
Five use-case families
Enabled by verified capability, distinguished by tactile sensing
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
14
Notes: To summarise the findings on one slide: the platforms are compatible at the flange; the single hard limit is electrical; there are two clean ways to resolve it; the hand variant is uniquely determined; the software reduces to a thin driver and bandwidth is fine; and five use-case families are enabled. All of this is established from specifications and analysis — which is exactly what a design study should deliver before hardware arrives.

## Slide 15
EVALUATION
A pre-registered three-stage plan (pending)
Stage 1
Interface verification
Current draw during motion; command latency & polling rate, TCI vs USB
METRICS
Mean/worst current · 95th-pct round-trip
→
Stage 2
Grasp benchmark
Fixed grasp types over ten objects at a taught pregrasp pose
METRICS
Success rate · failure modes · offset tolerance
→
Stage 3
Tactile demonstrator
Force-thresholded vs position-controlled grasp of deformable objects
METRICS
Crush rate · slip rate · contact force
No results yet. Each stage is tied to a specific claim, so its execution will confirm or refute that claim.
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
15
Notes: The validation is pre-registered in three stages. Stage 1 measures the electrical budget and the communication latency — it gates the choice between the two power concepts. Stage 2 benchmarks grasp success across a taxonomy and object set. Stage 3 compares force-controlled against position-controlled grasping on fragile objects. Each stage maps to a claim I've made, so running it will confirm or refute that claim. Again: no numbers yet — this is the plan.

## Slide 16
RISKS & LIMITATIONS
Stated plainly
KEY INTEGRATION RISKS
Tool over-current
Register limits; default to Concept B
Dropped serial frames
Shielded twisted pair, checksum + retry
Tool I/O misconfigured
Set communication mode in PolyScope
Object crush
Force-threshold grasp via tactile feedback
LIMITATIONS
No hardware built and no measurement taken — all quantitative results pending
The bandwidth figure is a first-order estimate, not a specification
Only grasps expressible by an underactuated six-DOF hand are in scope
A single right hand — bimanual tasks are excluded
Electrical figures are datasheet values; the true current profile must be measured
Stating limits plainly is deliberate — it keeps verified specs, reasoning, and planned work distinct.
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
16
Notes: On the left, the integration risks — the dominant one is electrical, and it's mitigated by the external supply; the rest are standard RS-485 and collaborative-tool concerns, each with a mitigation already in the design. On the right, the limitations, stated openly: no hardware, no measurements, an illustrative bandwidth estimate, a six-DOF subset of grasps, a single right hand. Admitting these is a strength, not a weakness.

## Slide 17
CONCLUSION
A buildable design, and a plan to prove it
01
Characterised both platforms
from vendor documentation, at the level integration needs
02
Derived the integration design
with the 5 A vs 1.5 A power-budget finding at its core
03
Mapped five use-case families
onto the hand's verified, tactile-enabled capabilities
04
Pre-registered the evaluation
three stages, each tied to a specific claim
Next step: execute Stage 1 the moment the hardware arrives — the current measurement that decides between the two power concepts.
Notes: To conclude: I characterised both platforms, derived an integration design built around the electrical finding, mapped five use cases onto verified capability, and pre-registered a three-stage evaluation. The contribution is a design and a validation plan. The very next step, the day the hand arrives, is the Stage 1 current measurement — because that single number decides whether we can power the hand from the flange or must use the external supply. Thank you — I'm happy to take questions.

## Slide 18
DEFENSE PREPARATION
Questions I am ready for
Q Why RS-485, not EtherCAT?
The tool flange carries RS-485; EtherCAT needs cabling the connector lacks.
Q Why not CAN FD?
CAN FD is the E4 build; it also cannot route through the tool connector.
Q Why RH56F1, not Allegro / Shadow?
Procured for the lab; hardware selection is outside this work's scope.
Q How are the power concepts validated?
Stage 1 measures current across representative motions before Concept A is used.
Q Expected TCI latency?
Not asserted — round-trip time is measured in Stage 1; the estimate is illustrative.
Q Which grasps with six DOF?
Only the taxonomy subset needing no independent abduction or in-hand reorientation.
RH56F1-E2R-T1 × UR5e — Integration Design & Evaluation Plan
18
Notes: I've prepared for the obvious questions: why RS-485 over EtherCAT or CAN FD (the flange decides it), why this hand (it was procured; selection is out of scope), how I'll validate the power design (Stage 1), what latency to expect (measured, not asserted), and which grasps six DOF can actually do (the reachable taxonomy subset).